## Slide 1
Boron Coated Straws imaging panel capability for neutron emission tomography for source localization inside radioactive drums
24/06/2021
M. BEN MOSBAH, C. ELEON, D. TISSEUR, H. BAKHABBA, A. DOGHMANE
Presentation #07-14

## Slide 2: Summary
Background and aims
Short state of art
MCNP Feasibility study
Experimental validation
Conclusion and future work

## Slide 3: Background and aims
Neutron imaging panel from Proportional Technology
7 boron coated straws (BCS) tubes (1 m height each) : nth +10B → α+ 7Li
Neutron interaction position sensitive (1 cm segmented counts)
Neutron emission tomography technique applied
Objective : neutron term source 3D mapping inside the drum
 reliable and robust estimation of mPu
Non destructive neutron measurement of nuclear waste [ref. 1]
Active and passive measurement system with neutron emission capability
mPu(g)
Criticality safety risk control, regulation of waste transport
workers’ radiation protection
Waste storage, retrieval of old waste
Radiological characterization of waste drums (50 L to 800 L)
Fissile (Pu-239) and other actinides (Pu-240) mass evaluation
Mass uncertainty reduction
 Better knowledge of the distribution of the nuclear material and the matrix effect
Neutron imaging Panel
BCS detectors
Mockup drum

## Slide 4: A short state of art [ref. 2]
MCNP design of complete BCS imaging panel measurement system
MCNP model
(empty drum)
Neutron counts = f(Z)
“Axial profile”
Z axis
Calculation versus experimental
Max deviation < 20%
Source Z position estimation
using “axial profiles”
One BCS tube
Zsource  centroid
“spatial resolution” 20 cm
Source radial position Rsource
using substraction between “FWHM” of opposite panels (FWHM(1-5))
Rsource = f(FWHM(1-5))
SNM clusters 2D map with
DDT (active measurement with neutron generator)
Exp. setup
SNM 1
SNM 2
graphite

## Slide 5: Neutron emission tomography : Deconvolution and 3D reconstruction Common to numerical and experimental images
Image processing
Imaging panel
Rotation
 = 30°
Neutron
source
12 “projections”
One projection
Merging
12 proj.
Deconvolution
kernel image
centred source
RTK retroprojection
Raw image
7*100 pixels
Rotating neutron emission tomography system
Reconstructed image
Richardson-Lucy
Algorithm*
Acquisition
*Richarson W.H., “Bayesian-Based Iterative Method of Image Restoration “ Journal of the Optical Society of America, Vol. 62, Issue 1, p. 55

## Slide 6
MCNP feasibility study : Geometry and setup

## Slide 7: MCNP feasibility study : neutron emission tomography station design
Initial MCNP model
9 Imaging panels (7 BCS tubes each)
New MCNP design
5 Imaging panels (21 BCS tubes)
No « shadow zones »
BCS tube
Imaging panel
Drum
not fully covered
Imaging panel
MCNP simulated images
Drum
fully covered by
21-tubes imaging panels
21 x 100 pixels
Z axis
Tubes

## Slide 8: MCNP feasibility study : results for 4 source configurations
9 cm
Z
reconstruction
Z
Tube
axis
Z centered source
252Cf
Z
Tube
axis
252Cf
“Bottom”
source
reconstruction
9 cm
Z
Tube axis
Z
“Top”
source
reconstruction
20 cm
59 cm
50 cm
29 cm
64 cm
9 cm
Z
73 cm
252Cf
60 cm
Z
252Cf
10 cm
reconstruction
Z
60 cm
22 cm
9 cm
14 cm
Two sources
AmBe
Feasibility validated !!

## Slide 9
Experimental validation

## Slide 10: Experimental setup
BCS imaging panel
Acquisition UI
Material
Image processing
softwares
CH2 25 cm large
7.5 cm width
Mockup
drum
Power supply
DAQ
Rotating plate
Spatial profile
(counting rate = f(Z))
Neutron counts 2D map
Data processing Python
The Reconstruction Toolkit
D=25.5 cm
H=74 cm

## Slide 11: Neutron source imaging : one source configuration
« Top » AmBe source
105 n.s-1
2D image after Richardson-Lucy Deconvolution
3D reconstruction
« Bottom » source AmBe source
105 n.cm-2.s-1
3D reconstruction
20cm
50cm
2D image after Richardson-Lucy Deconvolution
Acquisition time : 12*10 min

## Slide 12: Neutron source imaging : two sources configuration Axial positions
2D image after Richardson-Lucy Deconvolution
Mockup drum
CH2
BCS imaging panel
L= 74 cm
4,5cm
d
6,5cm
26cm
32.5cm
l= 25cm
e= 7,5cm
25,5cm
252Cf
Ambe
30cm
3D reconstruction
Acquisition time : 12*10 min
Source emissions 105 n.s-1

## Slide 13: Neutron source imaging : two sources configuration Radial positions
2D images after Richardson-Lucy Deconvolution
Acquisition time : 12*10 min
252Cf
AmBe
D=20, 30 and 40 cm
D=20 cm
D=30 cm
D=40 cm
40cm
34cm
22cm
Source emissions 105 n.s-1

## Slide 14
Concluding remarks

## Slide 15: Conclusion an future work
Demonstration of the Boron-coated Straw (BCS) imaging panel capability for neutron emission tomography :
  State of art : axial and radial source position determination ;
  Neutron emission tomography : MCNP feasibility validated;
  Experimental assay :
    Standard gamma tomography algorithms used
    Neutron sources in Mock-up drum measured with a rotating BCS imaging panel
    Successful neutron emission tomography :
      Single source @ different axial positions
      Two sources @ opposite axial (30 cm) and radial positions (20 cm)
  Prospects :
    Tests with organic, metallic and mixed matrices
    Tests with position sensitive He-3 tubes
    Optimization of Deconvolution and reconstruction processes (specific algorithms for neutrons,
    Machine and Deep Learning approaches)
    Test in active neutron mode (DDT technique)

## Slide 16: References
B. Perot et al. The characterization of radioactive waste: a critical review of techniques implemented or under development at CEA, France, EPJ Nuclear Sci. Technol. 4, 3 (2018)
C. Eleon et al. Boron-Coated Straws Imaging Panel Capability for Passive and Active Neutron Measurements of Radioactive Waste Drums, IEEE Transactions on nuclear science, Vol. 67, no. 9, September 2020
M. Cortesi et al. “Concept of a novel fast neutron imaging detector based on THGEM for fan-beam tomography applications ». Journal of Instrumentation, Volume 7, February 2012
D. Tisseur, N. Bhatia, N. Estre, L. Berge, D. Eck, E. Payan, Evaluation of a scattering correction method for high energy tomography, ANIMMA 2017, International Conference on Advancements in Nuclear Instrumentation Measurement Methods and their Applications, 19-23 June, Liège, Belgium.
M. Kistler, N. Estre, E. Merle, Simulated Performances of a Very High Energy Tomograph for Non-destructive Characterization of large objects, ANIMMA 2017, International Conference on Advancements in Nuclear Instrumentation Measurement Methods and their Applications, 19-23 June, Liège, Belgium.

## Slide 17
Thank you for your attention